## Slide 1
TIU Tracking System
Introduction
Intel's large and complex validation labs contain many Testing Interface Unit's(TIU) used in validating hardware. A TIU is a custom PCB that provides test points that a testing machine can probe. Since the hardware to be tested is varied, there exists a variety of different TIU's, and as such, finding a particular TIU is useful because, previously, the testing machine had to be broken down to identify the TIU it was using. The guiding requirements are that the system must be small, inexpensive, and low power.
Products
Test Results
Conclusions
Accomplish , contribution
The accuracy of the tracking system needs to be enhanced by considering antenna design and advanced locating algorithm. Noise filter can be implemented on both hardware and software to achieve desired performance.
Detector
Size: 3.5”x1”
ATMega328p MCU
RF12B transceiver at 434MHz
9V battery/adapter
Cost
Asset Tag
Size: 1”x1”x1”
ATMega328p MCU
RF12B transceiver at 434MHz
20mm coin cell battery
Battery life: 3 months
Cost
Chart: Battery voltage in one month
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Voltage | 5.8812 | 5.7647 | 5.6506 | 5.5387 | 5.429 | 5.3215 | 5.2161 | 5.1129 | 5.0116 | 4.9124 | 4.8151 | 4.7198 | 4.6263 | 4.5347 | 4.4449 | 4.3569 | 4.2706 | 4.1861 | 4.1032 | 4.0219 | 3.9423 | 3.8642 | 3.7877 | 3.7127 | 3.6392 | 3.5671 | 3.4965 | 3.4273 | 3.3594 | 3.2929
Capstone 2011
Sponsored by Intel
Advisor: Prof. Robert Daasch
Team Members:
Daniel Ferguson – Dung Le
Lynh Pham – Man Hoang – Tri Truong
Back-end Network
Controller
Primary link between the mesh network and the back end infrastructure
Communicates with mesh network
Executes the locating algorithm
Communicates with the Database
Fingerprint Algorithm
A progressively constrained, nearest neighbor algorithm, using Euclidean distance as the matching metric.
Heuristics, input and output filters are employed that further enhance the accuracy and reliability of the locating process
Web Application
Primary user interface with Interactive 2D map
Search TIU and detector via ID
Show battery level of all elements in the mesh network
Configure tag and detector
Configure geometry of tracking area
SQL Database
Stores locations and battery information of all tags and detectors
Stores user accounts
Design
Front End Network
Tags
Attached to TIUs.
Periodically broadcast.
When not broadcasting, in a low power state.
Detectors
Determine RSSI of broadcasting tags.
Must always be listening for a tag to broadcast.
Rebroadcasts the message, which results in messages always propagating toward the proxy.
Messages are relayed to the proxy via a controlled flooding mechanism.
Collision avoidance is achieved using time division.
Wi-Fi Proxy
Receives data from the mesh network and relays data to the controller.
Department of Electrical and Computer Engineering
Our system uses an RF transceiver mesh network to track mobile assets indoors. The system determines an asset’s current location by matching the RF fingerprint, based on signal strength, of a Tags periodic broadcasts with previously collected fingerprints stored in a database.
Why RF signal strength?
Radio Received Signal Strength Indication (RSSI) is a measurement of the amount of power received by antenna. Theoretically, distances can be approximated based on the relationship between transmitted and received signal strength.
We based our system on RF signal strength because alternative choices such as GPS, IR, and Acoustics either cannot work indoors, or requires line of sight. Also, low power RF transceivers are readily available.
For scalability, a mesh network of detectors relay all data to a centralized controller where locations of tags are calculated and saved in a database. An easy to use web application provides visualization of tag locations, as well as other maintenance details.
Approach
Controller
Detector
Tag
Users
Admin
Web App
Front-end
Back-end
Proxy
Database
Wi-Fi
Detector
  where
  d is the Euclidean distance between calibrated RSSI vectors and located RSSI vector.
  Sci is RSSI value received by detector i in calibrating phase
  Sli is RSSI value received by detector i in locating phase
  N is the number of detectors participating into the locating phase