## Slide 1
TIU TRACKING SYSTEM
Department of Electrical and Computer Engineering
Introduction
This system uses an RF transceiver network to track mobile assets indoors, where more obvious solutions, such as GPS, are unable to function. The system determines an asset’s current location by matching the RF fingerprint of its periodic broadcasts with previously collected fingerprints stored in a database.
Requirements
Asset tag’s size: 1” x 1” x 1”
Low power consumption
Accurate
Web application as user
interface
2D map display
Scalable tracking area
Low cost solution
This system uses an RF transceiver network to track mobile assets indoors, where more obvious solutions, such as GPS, are unable to function. The system determines an asset’s current location by matching the RF fingerprint of its periodic broadcasts with previously collected fingerprints stored in a database.
Approach
This system uses an RF transceiver network to track mobile assets indoors, where more obvious solutions, such as GPS, are unable to function. The system determines an asset’s current location by matching the RF fingerprint of its periodic broadcasts with previously collected fingerprints stored in a database.
Features
Indoor tracking area
Products
Test Results
Conclusions
The accuracy of the tracking system needs to be enhanced by considering antenna design and advanced locating algorithm. Noise filter can be implemented on both hardware and software to achieve desired performance.
Web Application
User and Admin interface
Interactive 2D map
Search TIU and detector via ID
Show battery level
Add and remove tag/detector
Change geometry of tracking area
SQL Database
RSSI-distance model or RF fingerprinting
Location update interval
Geometry of the tracking area
Identifications, locations, and battery levels of the TIUs
Detector
Size: 3.5”x1”
Use RF12B transceiver at
434MHz
Use MCU ATMega328p
Use 9V battery/adapter
Asset Tag
Size: 1”x1”x1”
Use RF12B transceiver at 434MHz
Use MCU ATMega328p
Use coin cell 20mm battery
Battery life: more than 1 month
Controller
Provide utilities to set up the system
Written in Java
Cross platform
Easy to use
Process data and calculate assets’ location
Chart: Battery voltage in one month
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Voltage | 5.8812 | 5.7647 | 5.6506 | 5.5387 | 5.429 | 5.3215 | 5.2161 | 5.1129 | 5.0116 | 4.9124 | 4.8151 | 4.7198 | 4.6263 | 4.5347 | 4.4449 | 4.3569 | 4.2706 | 4.1861 | 4.1032 | 4.0219 | 3.9423 | 3.8642 | 3.7877 | 3.7127 | 3.6392 | 3.5671 | 3.4965 | 3.4273 | 3.3594 | 3.2929
Capstone Project 2011
Advisor: Prof. Robert Daasch
Sponsored by Intel
Team members:
Lynh Pham – Daniel Ferguson
Dung Le – Man Hoang – Tri Truong
RF Mesh Network
User and Admin interface
Interactive 2D map
Search TIU and detector via ID
Show battery level
Add and remove tag/detector
Change geometry of tracking area
Wi-Fi Proxy
WiFly 802.11b/g at 2.4GHz
RF12B transceiver at 434MHz
MCU ATMega328p
Use 9V battery/adaptor
Fingerprint Algorithm
Calibrate and create a database of signal signature.
Locate by matching signal pattern
Interpolate calculated results
Design
Mesh Network Concept