## Slide 1: TIU Tracking System
Sponsor Intel
Advisor Prof. Robert Daasch
Team Daniel Ferguson
Man Hoang
Lynh Pham
Tri Truong
Dung Le

## Slide 2: Introduction
Problem statement
Key requirements
  Size
  Power
  Accuracy

## Slide 3: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 4: System Overview
Controller
+
Location Engine(s)
Detector
Users
Admin
Web App
Tag
Front-end
Back-end
Proxy
Database
Wi-Fi

## Slide 5: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 6: Hardware
Devices
  Tag
  Detector
  Proxy
Components
  RF12 transceiver
  ATmega328p MCU
  WiFly 802.11b/g transceiver
Schematic and layout by Eagle CAD
PCB by Sunstone Circuits

## Slide 7: Hardware
Tag
  RF12 transceiver
  ATmega328p MCU
  Size: 1” x 1” x 1”
  240mAh coin cell battery
Product
Main Board Layout
Breakout Board Layout

## Slide 8: Hardware
Detector
  RF12 transceiver
  ATmega328p MCU
  Status LED
  Size: 3.5” x 1”
Product
Layout

## Slide 9: Hardware
Proxy
  RF12 transceiver
  ATmega328p MCU
  WiFly 802.11b/g transceiver
  Breadboard prototype
  Ceramic antenna

## Slide 10: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 11: Firmware
Tag broadcasts
Detectors relay
Proxy forwards to Controller
Detector
Tag
Front-end
Proxy

## Slide 12: Firmware
Tag
  Mostly in low power state
  Periodically wakes up to broadcast
Detector
  Listen for messages from tags and other detectors
  Controlled flooding
  Collision avoidance via time division
Proxy
  Listens for messages from detectors
  Forwards messages to Controller
Generally
  All speak a common message format which includes
    Battery Information
    Infrastructure for a more sophisticated routing protocol
    Fixed length

## Slide 13: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 14: Software
Controller
+
Location Engine(s)
Web App
Back-end
Proxy
MySQL Database

## Slide 15: Software
Controller
  Collects data from Proxy
  Feed data to Location Engine
  Two operating modes
    Calibrating
      Collects RF signatures at calibration points
      Stores calibration data in a local database
    Locating
      Passes calibration data to Location Engine
      Collects and sorts data into packets
      Feeds the packets to Location Engine
      Stores results in MySQL Database

## Slide 16: Software
Location Engine
Theory
  Each location has a unique & consistent RSSI pattern
  Euclidean distance
Reduce aliasing by
  Referencing the nearest detector
  Interpolating between two closest locations
Fingerprint Matching Algorithm
Input Filter
Output Filter
Calibration Data
RSSI Data
Tag’s Location

## Slide 17: Software
Web App
  Functionalities
    Visualize tags’ and detectors’ locations
    Add, modify, and remove tags and detectors
    Configure the tracking area
  Design Goals
    Fast
    Simple
    Easy to use
  Technologies
    PHP
    HTML5, CSS3, JavaScript
  Why Web?
Notes: So, why a Web app but not a traditional window application?
Well, unlike a traditional window application, which requires different versions for different platforms, a web app can have only one version, and it can run virtually everywhere, from a mobile phone to a desktop.
Also, it doesn’t require any additional user installation, so it’s always there, always ready for users to access.

## Slide 18: Recap

## Slide 19: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 20: Deployment
Detector placement
Calibration density
Each tag has a unique ID with respect to other tags
Each detector has a unique ID with respect to other detectors
Proxy possible configurations
  Proxy must have access to LAN
  Proxy must create an Ad-Hoc Access point for Controller to connect to

## Slide 21: Deployment

## Slide 22: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 23: Results
Size: 1” x 1” x 1”

## Slide 24: Results
Power
  240mAh coin cell battery
  30mA transmit current
  40µA sleep current
  1sec broadcast interval
  3ms transmit window
  0.3% duty cycle

## Slide 25: Results
Accuracy
  Average 2m
  Less than 1m at calibration points
Notes: For accuracy, we conducted another experiment in a 12m x 6m area with a 3m calibration grid, and we found out that the average accuracy is roughly 2m.
The accuracy at calibration points is less than 1m for over 90% of the time. This indicates that if we calibrate the system at locations where the TIUs are usually placed, then probability of locating the TIUs accurately is very high.

## Slide 26: Agenda
System Overview
Hardware
Firmware
Software
Deployment
Results
Conclusions

## Slide 27: Conclusions
Antenna design
More testing
  Calibration density
  Detector placement
Improve testability
Different algorithms
Environment & signal strength

## Slide 28: Acknowledgement
Professor Robert Daasch
Alfonso Pereira & Sameer Ruiwale