## Slide 1
TIU Tracking System
Introduction
Intel's large and complex validation labs contain many Test Interface Units (TIUs) used in validating hardware. A TIU is a custom PCB that provides test points that a testing machine can probe. Since the hardware to be tested is varied, there exists a variety of different TIU's, and as such, finding a particular TIU is useful because, previously, the testing machine had to be broken down to identify the TIU it was using.
Products
Conclusions
We have a complete system that achieves small size, low cost, and battery life that exceeds 1 month. As for accuracy, when a tag is placed on exactly a location that was calibrated, success rates are at least 90%.
Further work to be done includes
Refine the testability of the system
Analyze antenna radiation pattern
Improve the robustness of the location algorithm
Detector
Size: 3.5”x1”
ATMega328p MCU
RF12B transceiver at 434MHz
9V battery/adapter
Cost: $30
Asset Tag
Size: 1”x1”x1”
ATMega328p MCU
RF12B transceiver at 434MHz
20mm coin cell battery
Battery life: at least 1 months
Cost : $25
Capstone 2011
Sponsored by Intel
Advisor: Prof. Robert Daasch
Team Members:
Daniel Ferguson – Dung Le
Lynh Pham – Man Hoang – Tri Truong
Design
Department of Electrical and Computer Engineering
The system uses an RF transceiver mesh network to track mobile assets indoors. The system determines an asset’s current location by matching the RF signal strength pattern of an asset tag’s periodic broadcasts with pre-collected patterns stored in a database.
Radio Received Signal Strength Indication (RSSI) is a measurement of the amount of power received by antenna. Signal strength based location method has several advantages over other methods such as GPS, IR, and Acoustics as it is easy to implement and does not require line of sight. Also, low cost RF transceivers are readily available.
For scalability, a mesh network of detectors relay all data to a centralized controller where locations of the tags are calculated and saved in a database. An easy to use web application provides visualization of tag locations, as well as other configuration details.
Approach
Controller
Detector
Tag
Users
Admin
Web App
Front-end
Back-end
Proxy
Database
Wi-Fi
Tags
Attached to TIUs
Periodically broadcast
When not broadcasting, in a low power state
Detectors
Listen to messages from tags and determine the RSSI values
Forward the messages to the proxy via a controlled flooding mechanism
Implements collision avoidance using time division
Wi-Fi Proxy
Relays data from the mesh network to the controller
SQL Database
Stores locations and battery levels of all tags and detectors
Stores user accounts
Chart: RSSI vs. Distance
| 1.5 | 3 | 4.5 | 6 | 7.5 | 9 | 10.5 | 12
-15dBm | 266 | 254 | 253 | 237 | 221 | 220 | 242 | 229
-21dBm | 248 | 224 | 223 | 205 | 205 | 205 | 214 | 220
Experiments
Proxy
ATMega328p MCU
RF12B transceiver at 434MHz
WiFly 802.11b/g transceiver
9V battery/adapter
Cost: $80
Controller
Receives RSSI and battery data from the mesh network
Executes the locating algorithm
Communicates with the Database
Fingerprint Algorithm
A pattern matching algorithm based on Euclidean distance
Employs heuristics and input output filters to further enhance the accuracy and reliability of the locating process
Web Application
Primary user interface with an interactive 2D map
Search TIUs and detectors via ID
Display locations and battery levels of all tags and detectors
Configure tags and detectors
Configure the tracking area