## Slide 1
TIU Tracking System
Introduction
Intel's large and complex validation labs contain many Test Interface Units (TIUs) used in validating hardware. A TIU is a custom PCB that provides test points that a testing machine can probe. Since the hardware to be tested is varied, there exists a variety of different TIU's, and as such, finding a particular TIU is useful because, previously, the testing machine had to be broken down to identify the TIU it was using.
Products
Conclusions
Size was addressed by constraining the PCB dimension, and using surface mount components.
Power was addressed by implementing low power states, moderating the broadcast rate, and restricting tag communication to one-way. We concluded that a tag can meet the requirement of lasting at least 1 month.
Accuracy has at least 90% success rates when a tag is placed on exactly a location was calibrated. This is good news, because TIU’s are always placed in the same orientation and location when they are inserted into the testing equipment.
Detector
Size: 3.5”x1”
ATMega328p MCU
RF12B transceiver at 434MHz
9V battery/adapter
Cost: $30
Asset Tag
Size: 1”x1”x1”
ATMega328p MCU
RF12B transceiver at 434MHz
20mm coin cell battery
Battery life: at least 1 months
Cost : $25
Capstone 2011
Sponsored by Intel
Advisor: Prof. Robert Daasch
Team Members:
Daniel Ferguson – Dung Le
Lynh Pham – Man Hoang – Tri Truong
Design
Department of Electrical and Computer Engineering
The system uses an RF transceiver mesh network to track mobile assets indoors. The system determines an asset’s current location by matching the RF signal strength pattern of an asset tag’s periodic broadcasts with pre-collected patterns stored in a database.
Signal strength based location method has several advantages over other methods such as GPS, IR, and Acoustics as it is easy to implement and does not require line of sight. Also, low cost RF transceivers are readily available.
For scalability, a mesh network of detectors relay all data to a centralized controller where locations of the tags are calculated and saved in a database. An easy to use web application provides visualization of tag locations, as well as other maintenance details.
Approach
Controller
Detector
Tag
Users
Admin
Web App
Front-end
Back-end
Proxy
Database
Wi-Fi
Controller
Receives RSSI and battery data from the mesh network
Executes the locating algorithm
Communicates with the Database
Fingerprint Algorithm
A pattern matching algorithm based on Euclidean distance
Employs heuristics and input output filters to further enhance the accuracy and reliability of the locating process
Web Application
Primary user interface with an interactive 2D map
Search TIUs and detectors via ID
Display locations and battery levels of all tags and detectors
Configure tags and detectors
Configure the tracking area
Tags
Attached to TIUs
Periodically broadcast
When not broadcasting, in a low power state
Detectors
Listen to messages from tags and determine the RSSI values
Forward the messages to the proxy via a controlled flooding mechanism
Implements collision avoidance using time division
Wi-Fi Proxy
Relays data from the mesh network to the controller
SQL Database
Stores locations and battery levels of all tags and detectors
Stores user accounts
Chart: RSSI vs. Distance
| 1.5 | 3 | 4.5 | 6 | 7.5 | 9 | 10.5 | 12
-15dBm | 266 | 254 | 253 | 237 | 221 | 220 | 242 | 229
-21dBm | 248 | 224 | 223 | 205 | 205 | 205 | 214 | 220
Experiments